## Slide 1
NOOS annual meeting 2018, Brussels
New developments concerning in-situ-data:
new methods and new buoys

## Slide 2: Outline
Baltic Sea Monitoring Buoy
North Sea Monitoring Buoy
Antifouling based on UV-LEDs
National Data center for sea state informations
Extended Method for wave data quality control

## Slide 3: Spar Buoy for the Baltic Sea
Oder Buoy II

## Slide 4: Spar Buoy for the Baltic Sea

## Slide 5: Multifunctional Monitoring Buoy - MoBo
Based on Lightbuoy LT 81
LiDAR-Windmeasurements
Meteorological data (airtemperature, humidity, airpressure)
Main Target Offshore-Windfarms
Substitution of a Met-mast

## Slide 6: Project: MoBo for the North Sea
Oceanographic Measurements:
Sensors at the tube-chair  cable connected
  ADCP (down-looking)
  CTDs incl. oxygen sensor
  Temperature sensor
  Radioactivity sensor
  Chemical Meas (pH, Chlorophyll, Nitrat,…)
Sensor-chain  Inductive data transmission
  CTDs incl. oxygen sensors
  Temperature sensors
  Chemical Meas (pH, Chlorophyll, Nitrat,…)
Botton frame  Acoustical data transmission
  CTDs incl. oxygen sensors
  ADCP (up looking)
Real-Time-Data

## Slide 7: Project: UV-LiBS

## Slide 8: Project: UV-LiBS

## Slide 9: Background RAVE Offshoreservice Project
Seastate Data Center
Co-operation with local agencies
Co-operation with Windfarms
Data Quality Control
NO1
AV0
BUD ●
●
●
Notes: RAVE Offshoreservice (BSH work packages):
Measurement service in alpha ventus
  oceanographic measurements
Design and implementation of new RAVE database
Data quality control
Design and implementation of new sea state data centre

## Slide 10: Data quality control (near real-time)
Sea state parameters which are tested:
Wave data
Sea state spectra
Aggregated data
  Significant wave height, peak period, ...
New methods to detect extreme waves in quality controlled in-situ meas.
Notes: water surface displacement = wasserspiegelauslenkung
copernicus project

## Slide 11: References
Copernicus Marine In Situ Team (2017). Copernicus In Situ TAC, Real Time Quality Control for WAVES, Copernicus in situ TAC.
IOOS (2015). Manual for Real-Time Quality Control of In-Situ Surface Wave Data. A Guide to Quality Control and Quality Assurance of In-Situ Surface Wave Observations. QARTOD.
SeaDataNet (2010). Data Quality Control Procedures.

## Slide 12: Actual status of quality control of wave data
# | Test Name | Data Type
1* | Date Test | all data
2* | Location Test | all data
3 | Completeness Test | all data
4 – 10 | (plausibility tests) | raw data
11 | (plausibility tests) | spectral data
12 – 16 | (plausibility tests) | aggregated data
*Copernicus Marine In Situ Team (2017)

## Slide 13: Actual status of quality control of wave data
# | Test Name | Definition
4 | Status Test | sensor status ok?
5 | Spike Test | moving window, val > 4.5std
6* | Range Test | sensor and physical range ok?
7 | Gradient Test | grad > 6 m/s
8 | Flat Line Test | ≥ 3 consecutive points
9* | Offset Test | large mean shift?
10** | Wandering Mean Test | Tz > 25 s?
raw data
*IOOS, (2015); **SeaDataNet (2010)
Notes: IOOS = QARTOD

## Slide 14: Detection of spikes
Spike → |value – mean| ≥ (4 + i*0.1) * std
Moving window method
  window width 200 s
  step width 100 s
Replace spikes with linear interpolated values
While loop until spike free
200 s
100 s

## Slide 15: Aktueller Stand Qualitätskontrolle Seegang
# | Test Name | Definition
5 | Spike Test | moving window, val > 4*std
raw data
window width: 200 s, step width: 100 s, 30-min with fS = 1.28 Hz |  | 
Good data = 1 | ≤ 0.25% (5 spikes) | ¦values – mean¦ > (4 + i*0.1) * std
Probably good = 2 | ≤ 0.66% (15 spikes) | 
Probably bad = 3 | ≤ 2.4% (55 spikes) | 
Bad data = 4 | > 2.4% (55 spikes) | 

## Slide 16: Aktueller Stand Qualitätskontrolle Seegang
spectral data
# | Test Name | Definition
11* | Spectrum Test | Is the energy for f ≤ 0.04Hz or f > 0.6Hz less than 5% of total energy?
*SeaDataNet (2010)

## Slide 17: Aktueller Stand Qualitätskontrolle Seegang
# | Test Name | Definition
12 | Range Test | Logical, physical, sensor range?
13* | Spike Test | ¦Vi-(Vi+1 + Vi-1)/2¦ - ¦(Vi+1 - Vi-1)/2¦
14* | Flat Line Test | Consecutive, identical values within 24hrs?
15* | Rate of Change in Time | ¦Vi-Vi-1¦+¦Vi-Vi+1¦ > 2*(2*std)
16** | Wave Periods | If TZ < TC or TP < TZ, flag = 4
aggregated data
*Copernicus Marine In Situ Team (2017) **SeaDataNet (2010)

## Slide 18: Detection of freak waves
Freak wave → aC / HS ≥ 1.25 (Haver, 2000)

## Slide 19: Definition of geometrical wave parameters
Dimensionless parameters | 
Wave steepness | sZ = H/L
Horizontal asymmetry | μH = aC/H

## Slide 20: Definition of Hilbert parameters
Instantaneous parameters | 
Amplitude | a(t)
Frequency | f(t)
Steepness* | sZ(t) = 2*a(t)/L(t)
„Wavelength“* | 
Instantaneous parameters | 
Amplitude | a(t)
Frequency | f(t)
Steepness* | sZ(t) = 2*a(t)/L(t)
„Wavelength“* | 
*Wilms (2017)

## Slide 21: Detection of freak waves

## Slide 22: Detection of freak waves

## Slide 23: Detection of freak waves

## Slide 24: Detection of freak waves
Notes: Find thresholds for sz(t)

## Slide 25: Conclusion & next steps
Summary of preleminary results:
Moving window method is a significant improvement to detect spikes, but it is not infallible
Geometrical and instantaneous parameters are valuable additional information to distinguish between spikes and freak waves
Next steps:
Further analysis and comparison with neighbouring sensors
Developing and implementing longterm quality control tests
Further development of web portal for sea state data centre
Notes: Entwicklung von Thresholds!

## Slide 26: Contact
Mayumi Wilms
Mayumi.Wilms@bsh.de
Tel. +49(0)40 3190-3288

## Slide 27
Thank you!