## Slide 1: River Project Aims (Bruce, 2014) 1. Make real-time observations of river fluxes available to partners 2. Make high quality historical data sets of observed fluxes and loads available to partners for hindcast studies 3. Assess the availability and applicability of prognostic river run-off data and make recommendations for further efforts 4. Develop best practices for applying river run-off data in coastal ocean forecasting

## Slide 2: In two words: - Access - Quality

## Slide 3: Access

## Slide 4: #1 : NRT observation of river fluxes and loads Data access: discharge. Managed by Deltares. √ Norwegian √ German √ Dutch √ Belgian http://noos.eurogoos.eu/observations/river-discharge-obs/ Pages linked: river level / hydrology England / Wales / N.Ireland Scotland Sweden

## Slide 5: #2 : Historical observations of river fluxes and loads Status unknown. How much history?

## Slide 6: #3 : Prognostic/hydrological data SMHI E-hype (Europe) 2014: e-hype 2.1 FREE 2016: e-hype3.0 model COMMERCIAL 2019: e-hype3.1 model VERY COMMERCIAL SMHI charges ”not for data, but for service”

## Slide 7: E-hype3 Data available from www
World-wide
http://hypeweb.smhi.se/
Europe (defunct)
http://hypeweb.smhi.se/europehype/time-series/download
New europe (thru login)
http://hypeweb.smhi.se/explore/historical/time-series/europe/

## Slide 8: E-hype3 data, Europe. Processed at DMI. 1. Historical run-off 30 years, 1981-2010 loads 11 years,2000-2010 Series, annual and calendar day climatology. 2. New historical / Interim (1980-) (1989-) 2011-2016/1 3. On-line 2016-present

## Slide 9: Other parameters water temperature : UNUSABLE Organic, inorganic, total N Particulate, soluble, total P kilos/month, need proper scaling depending on bio-model before use

## Slide 10: E-hype3 data – processed at DMI Not latest e-hype3 version. Run-off, 30 years, 1981-2010 Nutrient loads, 11 years, 2000-2010 Annual climatology Calendar day climatology Water temp: unusable. I think we can hand this out.

## Slide 11: E-hype3 data – SMHI pricing 30 years of history, v3.0, 1981-2010 free, but not on-line anymore 30 years of history, v3.1, 1989-present discharge – 4.000 € anything else – 17.000 € Real-time, daily download since 2016, annual fee discharge – 6.000 € / year anything else – 19.000 € / year https://www.smhi.se/en/services/open-data/hype-data-delivery-services-1.104448

## Slide 12: Question: How expensive may data get before it is to be regarded as inaccessible in project use, and in operational use. Is this nice-to-have, or need-to-have.

## Slide 13: E-hype3 data – pricing … Since charging is for service, one could imagine a centralized solution to minimize cost. Mercator / CMEMS will not purchase. Each ROOS or even partner on its own. At least until another hydrological model appears on the horizon …

## Slide 14: E-hype3 data – license agreement Permission to copy and distribute open data This would include anything that has been freely available on-line, even if it isn’t anymore

## Slide 15: E-hype helpdesk Close to non-existent. E-hype home page Pass-word protected areas. Stalls.

## Slide 16: Quality

## Slide 17: Studies by Bruce, Johan Söderkvist, myself In general, e-hype3 run-off is definitely useful. Be it real-time calendar day climatology monthly/annual climatology

## Slide 18: Example. Compare: E-hype3 model, SMHI 5 German river gauges, WSV

## Slide 19: WSV Data (Wasserstraβen und Schifffahrtverwaltung) https://pegelonline.wsv.de/ 20 locations in total One month of data freely available
Rhein, Elbe, Weser, Ems, Oder
2001-2016/5
Passed on to DMI by BSH thru this period (thanks)

## Slide 20: Any coastal segment with respect for itself it attributed an e-hype run-off estimate …

## Slide 25: Linear fit, correlation e-hype3 = A * wsv + B River A B CC Rhein 0.96 79 0.88 neutral Elbe 1.13 255 0.82 overpred. Weser 1.66 -76 0.93 OVERPRED. Oder 1.17 17.5 0.77 overpred. Ems 1.14 192 0.92 overpred.

## Slide 26: E-hype3 trend North Sea – Baltic Sea, 1981-2010
1981: 28048 m3/sec
-46.3 m3/sec / year

## Slide 27: River trends, 2001-2010 A*x + B fit WSV E-HYPE3 River A B A B Rhein -58.6 2540 -85.2 2658 Elbe 0.9 730 -11.7 1125 Weser -6.2 360 -14.2 543 Oder 14.1 444 10.8 721 Ems -1.8 90 -3.4 146

## Slide 28: River trends, 2001-2010 A*x + B fit

## Slide 29: Annual climatology Baltic run-off Jacob 2001, Meier 2006 ~16.500 m3/sec E-hype3, 1981-2010 16.183 m3/sec North Sea run-off E-hype3, 1981-2010 11.200 m3/sec I have not studied literature

## Slide 30: Nutrient loads. One fjord study. Citing: ”Afstrømning og næringsstoftilførsler til Limfjorden baseret på tre forskellige modeller” DCE Tech. Rep. 115/2018, Aarhus univ. Compares three run-off & loading models a. QNP-DK. Empirical, reliable, but coarse. b. SWAT, 82 sources c. E-HYPE3, 30 sources

## Slide 31: Limfjord nutrient loads… Conclusions 1. Run-offs are similar for all three models 2. SWAT overestimates nitrogen load 3. E-HYPE3 underestimates phosphorus load 4. Seasonal signal OK

## Slide 32: E-hype3 data – Further use Climatological run-off projected into future climate by transferring changes/trends in precipitation pattern.

## Slide 33: Baltic river runoff in future
Annual mean change 20%, follow Meier (2006)

## Slide 34: Historical data sets E-hype3.0 time series of run-off and nutrients downloaded

## Slide 35: Recommendations for further efforts o Better document real-time data access o Advocate for some sort of agreement between -SMHI and each ROOS o Consider if NRT data is worth the cost, or if climatology will do the trick o Encourage non-commercial hydrological model

## Slide 36: Best practices No progress.

## Slide 37: River Project Management. This is still not clarified, as is obvious. Up for grabs- I should like to get aquainted with any other run-off/load sources people might be using. Operational, hindcast, or climate