## Slide 1: Estimated Accuracy Numbers for CMEMS forecast
Christine Pequignet

## Slide 2: Estimated Accuracy Numbers (EAN)
Requirement for CMEMS forecast in the Quality Information document
mean (model minus observation bias) and standard deviations of errors
Assessed on 2 year analysis
Assessed on whole domain (or shelf only)

## Slide 3: Biogeochemical
variables | location | observation | RMS error
Chlorophyll-a | Full domain | Satellite observations | 0.94(log10)mg/m3
Chlorophyll-a | Continental shelf | Satellite observations | 0.97(log10)mg/m3
Sediments | Full domain | Satellite observations | 3.30 g/m3

## Slide 4: Waves
Estimated Variables | Location | Supporting observations | Mean Error | Error std
Significant wave height | Full domain | In situ platforms | -0.06m | 0.30m
Peak wave period | Full domain | In situ platforms | -0.24 s | 1.84s
Average zero crossing period | Full domain | In situ platforms | -0.57s | 0.61s
Significant wave period | Bay of Biscay | In situ platforms | 0.34s | 1.08s

## Slide 5: Physical properties
Variable | Location | Supporting observations | RMS error |  | Mean error (observation-model) | 
 |  |  | AMM15 | AMM7v9 | AMM15 | AMM7v9
M2 tidal harmonic (amplitude) | Whole region | Tide gauge data | 12 cm | 12 cm | -5 cm | -1 cm
M2 tidal harmonic (phase) | Whole region | Tide gauge data | 11° | 12° | 4° | -2 °
SST | Full domain | In situ observations | 0.48°C | 0.45°C | -0.01°C | -0.01°C
 | Continental shelf | In situ observations | 0.54°C | 0.51°C | -0.02°C | -0.02°C
SST | Full domain | OSTIA satellite L4 | 0.34°C | 0.34°C | -0.08 | -0.06
T profiles | Full domain | In situ observations | 0.43°C | 0.47°C | 0.02°C | -0.04°C
S profiles | Full domain | In situ observations | 0.11 | 0.13 | -0.01 | 0.01
SSH | Off-shelf | Altimeter from satellite | 0.09 m | 0.09 m | 0.01m | -0.01m
 | Continental shelf | Altimeter from satellite | 0.13 m | 0.13 m | -0.02 m | -0.06 m
Mixed layer depth | Full domain | In situ observations | 121.77 m | N/A | 21.7m | N/A
 | Full domain Period: May-Oct | In situ observations | 22m | N/A | -11 m | N/A

## Slide 6: Issues
Poor coverage of some variables
How meaningful is one number for all domain, all seasons
For some variables % can be reported and be more meaningful
Problem with assessment and high resolution