## Slide 1: Multi-Model-Ensemble in NOOS
NOOS Annual Meeting, Brussels, 19-21th November 2018
Inga Golbeck
Federal Maritime and Hydrographic Agency (BSH)

## Slide 2: MME of forecast products : Overview
„Poor-man‘s ensemble“: MME based on several independent ocean forecasting models for North Sea (8 members) and Baltic Sea (10 members)
Data and parameters:
  Hourly 48h-forecasts:
    Sea surface temperature, - salinity, - currents
    Sea bottom temperature, - salinity
    Water level (only BOOS)
  Mass and salt transports (daily data)
Financing & Partners of NOOS & BOOS MME:
  MME developed in Copernicus Marine Service
  MME lead: BSH
Aims and benefits of MME:
  Temporal / spatial distribution of forecast uncertainties
  Supplement to single-model validation
  Best estimates of forecasts (e.g. water level)
  Detection of forecast products drifting away from MME
Documentation:
  Golbeck, I., Li, X., Janssen, F. et al. (2015) 65: Uncertainty estimation for operational ocean forecast products—a multi-model ensemble for the North Sea and the Baltic Sea, Ocean Dynamics
Website NOOS MME:
  http://noos.eurogoos.eu/community-products/multi-model-ensemble-of-forecast-products/

## Slide 3: MME: Metrics
Uncertainty estimates / forecast ensemble statistics – daily update
  MME mean, median, min, max, standard deviation
  Bias between MME median & ensemble members
  Individual metrics for transports, currents
Validation – monthly update
  CMEMS in-situ data: Temperature, salinity (bottom, surface)
  CMEMS L3 satellite data: SST
“Warning System” – daily update
  Based on spatio-temporal difference between MME median & ensemble members
  see: https://www2.bsh.de/aktdat/community_products/noos/warningsystem/Warning_system_TS_NOOS.pdf
<
<
<
<
<

## Slide 4: Example „Warning-system“ (1/2)
Layout updated: information about positive or negative deviation (+ : forecast product warmer/saltier than MME)
Overview of warnings of the last 30 days – daily update
1st warning “Daily-median-test”: Difference to MME median ± 2*standard deviation
2nd warning “30days-threshold-test”: Differences to mean differences of last 30 days ± 2*mean standard deviation

## Slide 5: Example „Warning-System“ (2/2)
Example: Sea surface temperature
Drifting CMOD forecast in warning system detected > SST too cold

## Slide 6: MME of multi-year products
Present time period: Feb 2002 – June 2012
Parameters: temperature, salinity
Resolution: 4D data; monthly mean
Target grid: 3D interpolation on CMEMS grid
Weighting with “KLIWAS North Sea climatology” (1873 – 2013) - gridded set of yearly and monthly mean hydrographic and surface meteorological data
POLCOMS
NEMO
FOAM
NORWECOM
ROMS
IBIRYSV1
http://noos.eurogoos.eu/community-products/multi-model-ensemble-of-multi-year-products/
Will be updated to:
CMEMS reanalysis time period: 1992 – 2016
Include only „CMEMS products“:
  FOAM AMM7 (NWS MFC)
  IBIRYSV1 (IBI MFC)
  POLCOMS (PML)
  NEMO (NOC)
  Possibly product from Global MFC
Improve weighting

## Slide 7: BOOS MME of sea level – „best estimate“
24 BOOS stations
BIAS removed
RMSE of MME weighted mean
Comparison of forecasts with MME weighted mean  „best estimate“
Calculation of weights using RMSEs of the forecasts 2 days before present

## Slide 8: BOOS MME of sea level - validation
Monthly values and daily time series of RMSEs
MME provides best estimate at most stations

## Slide 9: Outlook
Is there an interest for having an MME of wave parameters?
  E.g. wave period, significant wave height
Should we extend the BOOS MME of water level to the NOOS area (without being a competitive product to MATROOS)?
  MME WL has proven to yield „best estimates“ at most stations
  MME WL is frequently used by BSH and DMI operational storm surge forecasting centers
  Users are asking to include more stations (also in NOOS area)