## Slide 1: Strategies for optimising operational decisions using probabilistic marine forecasts
Dr Edward Steele
Presented by Dr John Siddorn

## Slide 2
Higher cost ($$$)
Lower cost ($)
Departure date
Correct identification of calm weather windows can save many thousands of dollars per day in unplanned downtime, allowing large savings if decisions are made as early as possible, but only when the science is employed to best effect…
Background

## Slide 3
At present, most offshore industry decisions based on deterministic forecasts…
Probabilistic forecasts aim to quantify uncertainty dynamically and are more suitable for maximising the opportunity for planning…
…but due to perceived complexity, products are often (over) simplified, masking the actual values on which to make an objective decision.

## Slide 4
Leveraging as much science as possible (without the user knowing it!)
Examples:
Using relative economic value of forecasts to
determine when to take action upon it;
Using weather pattern typology to identify calm
weather windows for local operations;

## Slide 5
Combining customer insights with ensembles
X
Deterministic
“simplicity”
Probabilistic
“skill”
Quantitative useful/usable products
Products

## Slide 6
Deterministic
“simplicity”
Probabilistic
“skill”
Quantitative useful/usable products
Products
Continuous forecasts can be turned into binary forecasts by applying a user-relevant threshold.
With binary forecasts, action is clear:
Event forecast – take action
Event not forecast – take no action
With ensemble forecasts a decision must be made on which probability value to act on.
Combining customer insights with ensembles – relative economic value

## Slide 7
 | Yes | No
Yes | a | b
No | c | d
Where:
 | Yes | No
Yes | C | C
No | L | 0
Observed
Observed
Forecast
Forecast
2x2 contingency table:
Cost-loss assignments:
The Relative Economic Value allows impact of an adverse weather event to be estimated in industry-relevant (economic) terms:
Cost incurred whenever decision made to protect (irrespective of occurrence);
Loss incurred whenever the event occurs and the decision made not to protect;
Value compared to climatological baseline (V=0) and expressed as fraction of the maximum obtained from using a perfect forecast (V=1).
Combining customer insights with ensembles – relative economic value

## Slide 8
The Relative Economic Value as a function of C/L, calculated from forecasts made 3 days ahead for 10 locations over 1 year (adverse event: Hs > 3.5m in 24 hours).
Highest value from ensemble: user gains some benefit over best-estimate forecast and climatology.
Thin black lines = individual probability thresholds
Thick black line = optimum probability threshold (maximizes V at each C/L)
Dashed red line = result from deterministic forecast
Combining customer insights with ensembles – relative economic value

## Slide 9
The Relative Economic Value as a function of C/L, calculated from forecasts made 3 days ahead for 10 locations over 1 year (adverse event: Hs > 3.5m in 24 hours).
Highest value from ensemble: user gains some benefit over best-estimate forecast and climatology.
The Relative Economic Value as a function of probability (fixed C/L = 0.1 (typical of offshore operations).
Value is maximum when P = 0.2: user gains maximum benefit by postponing operations when more than 5 of 24 ensemble members predict the adverse event or vice versa.
Combining customer insights with ensembles – relative economic value

## Slide 10
Proceed
Protect
Visualisation
Compare forecast
and observations
Verification of performance
Establish threshold
for future decisions
(update)
Combining customer insights with ensembles – relative economic value

## Slide 11
Benefits to offshore asset managers
Actual decision-making often more complex than a simple yes/no, but the C/L framework offers a sensible basis for handling probabilities.
Greater reliability of probabilistic forecasts over deterministic forecasts days to weeks ahead offers the opportunity for more timely decision-making.
Useful in coordinating interrelated components of operations (e.g. vessels / supplies) or starting installation shut-down preparations (cancelling activities / removing non-essential personnel) early.

## Slide 12
A weather pattern approach to assisting decision-making – “Decider”
Cyclonic westerly
(Mild, wet and windy conditions)
Cyclonic north-westerly
(Cool and showery conditions)
Cyclonic northerly
(Cold and showery conditions)
Constraining an otherwise ambiguous set of ensemble members can be achieved by grouping these data according to some criteria, e.g. weather pattern.
Weather pattern: “one of many broad-scale atmospheric circulation types over a particular area – that differs in characteristics from other weather pattern classifications over the same domain –and can vary on a daily basis”.

## Slide 13
The Met Office has established a set of 30 predefined weather pattern types by clustering 154-years of daily averaged Mean Sea Level Pressure Anomalies.
These are used for the examination of variability within large-scale circulation types up to several weeks ahead, and numbered by annual historic occurrence.
A weather pattern approach to assisting decision-making – “Decider”

## Slide 14
Ensemble members are assigned to the closest of 30 weather pattern definitions, simplifying the data into a sequence of probabilities.
Occurrence of each weather pattern may be correlated with the viability of different types of offshore operations at a local scale.
http://exvmogwebprod01/~regimes/decider/home.shtml
A weather pattern approach to assisting decision-making – “Decider”

## Slide 15
Example set of KDEs of daily maximum significant wave height for each of the historical weather pattern classifications for the location of interest (Central North Sea).
A weather pattern approach to assisting decision-making – “Decider”

## Slide 16
A weather pattern approach to assisting decision-making – “Decider”

## Slide 17
Example forecast of the probability of the significant wave height being less than various maximum limits as a function of lead time.
Depending on operational limits, the user must reference that particular row of the table, with the decision to proceed with activity based on the probability of calm conditions exceeding their (pre-defined) confidence level.
A weather pattern approach to assisting decision-making – “Decider”

## Slide 18
Weather pattern analysis offers the opportunity for contingencies to be established.
Useful in anticipating how long equipment / personnel will remain offshore if conditions are favourable at the outset but delays in preceding operation mean weather windows are misses, or when to plan for re-deployment following an installation shut down.
Knowing the odds of having a sustained period of limited flying will also allow asset managers to re-prioritise supplies / personnel changes.
Benefits to offshore asset managers

## Slide 19
Conclusion
The key to effective customer application is synthesising the science.
To enable users to assess weather risks, two established methods for the efficient interpretation of probabilistic data based on cost-loss and regime analysis are described and applied to ocean wave forecasting;
  Cost-loss analysis offers an objective method of determining ensemble thresholds;
  Regime analysis offers an intuitive approach to simplifying ensemble forecasts;
Appropriate use of these methods will enable more timely decision-making and therefore help reduce operational costs for the offshore energy sector;
Ultimately, planning will be best supported by the use of forecasts across all timescales;

## Slide 20: Thank you for listening!
Dr Edward Steele
edward.steele@metoffice.gov.uk
Find out more in our recent publications:
Steele et al. (2017) Making the most of probabilistic marine forecasts on timescales of days, weeks and months ahead. DOI: https://doi.org/10.4043/27708-MS.
Steele et al. (2018) Using weather pattern typology to identify calm weather windows for local operations. DOI: https://doi.org/10.4043/28784-MS.