## Slide 1: Storm Surge Risk Tool based on ICON-EPS - Probabilistic storm surge forecast Ludwig Schenk, Stephan Dick, BSH
NOOS Annual Meeting, Brussels, 19-21th November 2018

## Slide 2
ICON is the global weather model of the German Weather Service (DWD)
EPS…Ensemble Prediction System (since beginning of 2018)
  Different forecast scenarios by variation of boundary conditions and different model physics (40 members/realizations)
  Resolution: 6 h, 0,75°grid (interpolated)
  180 h prediction period (7,5 days)
  2 runs a day (0 UTC and 12 UTC)
  We use only u and v of 10 m wind (main storm surge player)
Storm Surge Risk Tool based on ICON-EPS

## Slide 3
Storm Surge Risk Tool developed by University (FU) Berlin
Processing of meteorological ICON-EPS data (3 step method)
Probabilistic assessment for wind velocities that could cause storm surges in German Bight
Tool for long term forecasts of Water Level Prediction Service at BSH
Coupled to statistical forecast method
Up to now: no model runs with ocean model ensemble!
Storm Surge Risk Tool based on ICON-EPS

## Slide 4: First step: Tracking
Storm-Box:
26 N – 79 N
69 W – 49 E
Tracking procedure detects storm tracks of wind velocity maxima
Different criteria:
  wind velocity exceeds 98 percentile of pre-calculated wind statistic
  Covered area > 150.000 km²
  Storm duration > 24 hrs
Reference: Leckebusch et. al (2008)
ICON-EPS grid

## Slide 5
Example: 23.10.2018
First storm surge of season 2018/19

## Slide 6: First step: Tracking
Storm-Box:
26 N – 79 N
69 W – 49 E
Tracking procedure detects storm tracks of wind velocity maxima (not pmin)
Storm track criteria for member:
Vmember, k > 98. Perc. of vk
Area min. 150.000 km²
Persists 24 h or longer
Distance between 2 time steps (6h) < 600 km
Combined to storm tracks by nearest neighbor routine
More about tracking: Leckebusch et. al (2008)
All storm tracks of 40 members in 180 h forecast period of ICON-EPS

## Slide 7: Second step: Clustering of tracked storms
Storm tracks of the EPS members are combined to clusters.
  Time window < 18 h.
  Spatial window < 1500 km
  If a storm track hits the German Bight the Storm Surge Severity Index - SSSI will be calculated.

## Slide 8
SSSI-Box:
53.5 N – 56 N
4 E – 9 E
Effective wind velocity = 295°:
Wind direction which causes statistically highest surges at Cuxhaven
Third step: Storm Surge Severity Index - SSSI
SSSI(t):
Index for severity of storm velocity from 295° in German Bight
(> 0 if velocity exceeds 98 percentile of 295° wind statistics)
  k = grid box
  proj(vk,t) = effective wind velocity of 295°
  proj(vperc,k) = 98 percentile of proj(vk,t)
  Ak = area of grid box

## Slide 9
SSSI-values and probabilistic analysis with BSH-SFRT (Example of Oct. 2018 -96 h)
Probability that members exceed SSSI value > 0 (storm in German Bight from 295°)

## Slide 10
SSSI-values and probabilistic analysis with BSH-SFRT (Example of Oct. 2018 -1 week)

## Slide 11
SSSI-values and probabilistic analysis with BSH-SFRT (Example of Oct. 2018 -96 h)

## Slide 12
SSSI-values and probabilistic analysis with BSH-SFRT (Example of Oct. 2018 -60 h)

## Slide 13
Measurements:
Nearly storm surge Cuxhaven 03.10.2018 12:09 -> 131 cm
Storm surge Hamburg St Pauli 23.10.2018 15:43 -> 161 cm
SSSI-values and probabilistic analysis with BSH-SFRT (Example of Oct. 2018 -36 h)

## Slide 14
Application for forecaster
See also: KFKI Project MUSE (2005)

## Slide 15
Application for forecaster

## Slide 16
See also: Müller-Navarra et al. (97)
Application for forecaster

## Slide 17: Summary
Storm Surge Risk Tool is based on ICON EPS global ensemble forecasts of DWD
  40 members, 180 h prediction period
Long term assessment for storm surge forecasts using a 3 step method:
  Storm tracking of each EPS member
  Storm clustering
  Calculation of SSSI if storm tracks hit SSSI-Box (German bight)
Up to now no runs with ocean model ensemble, but planned

## Slide 18
Thank you!
Hamburg Fischmarkt
13.09.2017
Foto: dpa, chc

## Slide 19: Literature
Gregor C Leckebusch, Dominik Renggli, and Uwe Ulbrich. Development and application of an objective storm severity measure for the northeast atlantic region. Meteorologische Zeitschrift, 17(5):575–587, 2008.
Bork, I. S.H. Müller-Navarra, Sturmflutsimulationen In: Modellgestützte Untersuchungen zu Sturmfluten mit sehr geringen Eintrittswahrscheinlichkeiten an der Deutschen Nordseeküste (Abschlussbericht MUSE, 2005)
Müller-Navarra, S.H. & Giese, H.. Improvements of an empirical model to forecast wind surge in the German Bight., Deutsche Hydrographische Zeitschrift (1999) 51: 385.

## Slide 20
Application for forecaster

## Slide 21
See also: Müller-Navarra et al. (97)
Application for forecaster

## Slide 22
Application for forecaster

## Slide 23
Application for forecaster