## Slide 1: Operational Ocean forecasting at BSH Ina Lorkowski (ina.lorkowski@bsh.de) and the operational modelling group
NOOS Annual meeting 2019, Hamburg

## Slide 2
wind, air pressure, air temperature,
cloud coverage, specific humidity
Circulation models (BSHcmod, BSH-HBM)
for North-/Baltic Sea and river Elbe
(5km + 900m + 90m grid, 3-D, baroclinic)
Surge Model (BSHsmod)
for the North Sea
(5km grid, 2-D, barotropic)
Model data archive currents, water levels, salinity, temperature, ice data, meteorological data
Lagrangian drift and dispersion model (SeatrackWeb)
for oil, drifting objects and conservative substances
Eulerian dispersion model
(BSHdmod.E/BSH-HBM)
for conservative substances, suspended matter
Additional forcing data:
tidal predictions external surges (from BSHsmod.na) river input (BfG, SMHI)
Meteorological models of DWD (ICON)
forecasts up to 180 hours
external surge, tidal constituents,
river runoff
Operational modelling system at BSH

## Slide 3: Main applications
Circulation modelling
Drift
modelling
Water level &
storm surge modelling
Dispersion
modelling
Biogeochemical modelling

## Slide 4: General overview: Operational model system
3D (& 2D) ocean circulation models based on BSHcmod & HBM (HIROMB-BOOS-MODEL)
dx = 5 km 36 levels
dx = 900 m 25 levels
Arakawa-C-Grid
2-way dynamical nesting
wetting & drying
dynamical vertical coordinates Kleine, 2003
dynamical ice module Hibler,1979
highly efficient code (OMP & MPI) Berg and Poulsen, 2012
dx = 90 m 7 levels
2-way nesting
1-way nesting
Advection by flux-corrected transport scheme
k-ω-turbulence model Berg, 2012
Open boundary:
  Tides (14 constituents)
  Surge (from internal NOA-surge model)
  Temperature/Salinity Janssen et al., 1999
NetCDF output
Dick et al., 2001: The Operational Circulation Model of BSH (BSHcmod) – model description and validation

## Slide 5: Product examples: (surface) currents
Information on currents is provided:
in different resolutions
for several subregions
in several formats (ASCII, NetCDF, Grib, maps)
via different channels (Web, Ftp, WMS)
contact:
opmod@bsh.de

## Slide 6: Product example: water level
Notes: Sandbag damming, crevasse = Deichbruch

## Slide 7
DA method: Ensemble Kalman filter
Observation data: 2 SST satellite data sets The choice of the data set is based on the availability of the satellite data
HBM-PDAF
Ensemble Kalman filter: Local Error Subspace Kalman Transform Filter (LESKTF) scheme (Nerger et al., 2012) in the Parallel Data Assimilation Framework (PDAF)
Ensemble size 8 (sufficient for good results)
Localization in horizontal and vertical
SST images are assimilated every 12 hours on a pre-operational basis
Advanced Very High Resolution Radiometer (AVHRR), which is processed, gridded and quality controlled by the BSH satellite data service
L3 CMEMS SST product
Pre-operational Dataassimilation
Notes: Folie raus?

## Slide 8: SST Validation of DA results
Daily validation shown on the BSH-intranet
Reduction in bias
SST
BIAS (model - obs)
OBS
Without DA
With DA
With DA

## Slide 9: Common driftmodel development

## Slide 10: Container-Drift
Notification: 4.01.2017, 7:45:
Loss of 5 container
10% above sea surface
Juist
Norderney
Baltrum
Langeoog
Ostfriesland

## Slide 11: Wave bouy

## Slide 12: Validation campaigns 2015 und 2017

## Slide 13: Eulerian transport model derived from HBM: moving source
To understand the distribution of washwater from gas cleaning systems on vessels
Notes: Sandbag damming, crevasse = Deichbruch

## Slide 14: Biogeochemical modelling ERGOM
coupled to HBM running pre-operational once a day
Bottom oxygen maps as internal BSH product to support measurement campaigns
Product development for MSFD
Carbon cycle in test phase

## Slide 15: Product examples – bottom oxygen
bottom oxygen before (left) and after (right) storm Sebastian moved across the German Bight

## Slide 16: Comparison with cruise data summer 2015

## Slide 17: Product examples – exceedance of critical values describing the status of the marine environment
# days in 2012 on which critical values for total nitrogen were exceeded

## Slide 18: Copernicus Marine and Environmental Service (CMEMS)
marine.copernicus.eu
BSH modelling group contributing to Baltic Sea Forecasting Center and North West Shelf Forecasting Center
  Biogeochemical model development and Data Assimilation (BAL)
  Coupling NEMO 4.0 and ERGOM (BAL)
  Product quality (BAL, NWS)
  Multi model ensemble (BAL, NWS)

## Slide 19: (Climate) Projection Service for Waterways and Shipping
Part of the „German Strategy for Adaption to Climate Change“ (DAS)
participation of four German Federal Agencies
Goal:
  establishment of a forecasting and projection service for climate, extreme weather and coastal & inland waterbodies in Germany
Tasks:
  further development of the ocean component for the coupled climate model ROAM:
    NEMO Nordic V3.3  NEMO GCOAST V4.0 (with nesting and wetting & drying)
  case studies and scenario runs
  impact of climate change on German coastal regions, see examples:
max. water level during hindcast period 1997-2015 in German Bight
# of days with SST > 19oC in 2009

## Slide 20
Thank you!