## Slide 1
Mayumi Wilms, Kai Herklotz
National Sea State Portal & Wave Data Quality Control
NOOS Annual Meeting 2019
BSH Hamburg, 17.10.19

## Slide 2: Background & Objective
Research project RAVE Offshoreservice (02/2017 – 01/2020)
  Work package 4: Extension of the monitoring network and analysis of sea state data
Public access to a large, quality-controlled in situ sea state database with application-oriented sea state presentations and analyses.
Target groups:
  Offshore Industry
  Universities / Research Institutes
  Government Agencies
  Maritime Sector (sea shipping, marine)
Notes: Federal Ministry for Economic Affairs and Energy

## Slide 3: Background & Objective
● NO1
● AV0
BUD ●
BUH ●
N7S ●
15 stations = 9 BSH + 3 FINO + 3 RAVE
Notes: Marine Environmental Monitoring Network
The sea state data center secures the data from the monitoring network, checks it uniformly for quality, makes it available and generates data products for the users.

## Slide 4: Background & Objective
directional waverider buoy, DWR-MKIII, Datawell
acoustic wave and current profiler, AWAC, Nortek
directional radar, WG4/WG5, RADAC
DWR Buoy
AWAC Profiler
3D RADAC
1D RADAC
Notes: The sea state data center secures the data from the monitoring network, checks it uniformly for quality, makes it available and generates data products for the users.

## Slide 5: Current Status of the Sea State Portal
png / svg
netCDF / csv
Notes: Sea state portal in progress, currently still on the test environment on the server
Sea state data products dynamically created, see next slides; further products are planned

## Slide 6: Current Status of the Sea State Portal
COPERNICUS (SeaDataNet, OceanSITES, Argo)
Notes: Copernicus
SeaDataNet / OceanSITES / Argo

## Slide 7: Current Status of the Sea State Portal
Products:
histogram Hs
directional wave rose Hs vs. Dirp
scatter plot Hs vs. Dirp, Hs vs Tp
yearly
selectable time range

## Slide 8: Data quality control (automatic, real-time)
Sea state parameters which are tested:
Wave data
Sea state spectra
Aggregated data
  Significant wave height, peak period, ...

## Slide 9: Data quality control (automatic, real-time)
# | Test Name | Data Type
1* | Date Test | all data
2* | Location Test | all data
3 | Completeness Test | all data
4 – 10 | (plausibility tests) | raw data
11 | (plausibility tests) | spectral data
12 – 16 | (plausibility tests) | aggregated data
*Copernicus Marine In Situ Team (2017)

## Slide 10: Data quality control (automatic, real-time)
# | Test Name | Definition
4 | Spike Test | moving window, val > 4.5std
5* | Range Test | sensor and physical range ok?
6 | Flat Line Test | ≥ 3 consecutive points
7 | Gradient Test | grad > 6 m/s
8* | Offset Test | large mean shift?
9** | Wandering Mean Test | Tz > 25 s?
10 | Status Test | sensor status ok?
raw data
*IOOS, (2015); **SeaDataNet (2010)

## Slide 11: Data quality control (automatic, real-time)
spectral data
# | Test Name | Definition
11* | Spectrum Test | Is the energy for f ≤ 0.04Hz or f > 0.6Hz less than 5% of total energy?
*SeaDataNet (2010)

## Slide 12: Data quality control (automatic, real-time)
# | Test Name | Definition
12 | Range Test | Logical, physical, sensor range?
13* | Spike Test | ¦Vi-(Vi+1 + Vi-1)/2¦ - ¦(Vi+1 - Vi-1)/2¦
14* | Flat Line Test | Consecutive, identical values within 24hrs?
15* | Rate of Change in Time | ¦Vi-Vi-1¦+¦Vi-Vi+1¦ > 2*(2*std)
16** | Wave Periods | If TZ < TC or TP < TZ, flag = 4
aggregated data
*Copernicus Marine In Situ Team (2017) **SeaDataNet (2010)

## Slide 13: Data quality control (automatic, real-time)
detailed quality flag:
a sequence of flags which contains each test result of the 16 real-time quality control tests
111 0000000 0 14111
final quality flag:
worst flag in the detailed quality flag
4

## Slide 14: Outlook
  Implement quality control for heave and spectral data
    “connect” parameters: if heave data is flagged as bad, spectral and aggregated data is flagged as bad
  Develop quality control tests for delayed mode
  Go live with sea state portal, currently still on the test environment on the server
  Implement further sea state data products (further analyses)
  Include current data and water level data (open sea)

## Slide 15
Vielen Dank!

## Slide 16: References
Copernicus Marine In Situ Team (2017). Copernicus In Situ TAC, Real Time Quality Control for WAVES, Copernicus in situ TAC.
IOOS (2015). Manual for Real-Time Quality Control of In-Situ Surface Wave Data. A Guide to Quality Control and Quality Assurance of In-Situ Surface Wave Observations. QARTOD.
SeaDataNet (2010). Data Quality Control Procedures.

## Slide 17: Data quality control (automatic, real-time)
Spike → |value – mean| ≥ (4 + i*0.1) * std
Moving window method
  window width 200 s
  step width 100 s
Replace spikes with linear interpolated values
While loop until spike free
200 s
100 s

## Slide 18
Aktuelles Monitoringnetzwerk
©wpd / Paul Langrock
©innogy SE
alpha ventus
Nordsee One
Butendiek
Notes:   Messungen in Nordsee One und Butendiek laufen einwandfrei
  Projektziel OpenRAVE:
    4 weitere Windparks dazu gewinnen
    Fokus auf Strömungs- und Wasserstandsmessungen legen
    Automatische Qualitätskontrolle für Strömung und Wasserstand einrichten