## Slide 1: Recent developments in the CLAIM project
Jens Murawski, Jun She (DMI)
NOOS Annual Meeting
BSH Hamburg, 17.10.2019
CLAIM: Cleaning marine Litter by developing and Applying Innovative Methods

## Slide 2
CLAIM: Cleaning marine Litter by developing and Applying Innovative Methods
Cartoon from Wulf Morgenthaler

## Slide 3: CLAIM: project overview H2020 Innovation Action
WP1
WP3
WP2
WP5
Forecasting
Technology:
    Nanotech coating
Pyrolyzer
Booms
Filtering
Ferry-Boxes
Validation &
Demonstration
Ecosystem
Approach: Foodweb
Economical feasibility
Social acceptance
WP6
Outreach
WP4

## Slide 4
Technological solution for cleaning Macro Plastics
Floating booms and marine litter collection and recovery system (New Naval)
prototype at Kifissos river in Athens, Greece.
Small Scale Pyrolyser
application on small-sized vessels and in harbors.
transforms plastic waste into combustible gas, which can be used as energy source
suitable for marine litter that cannot be recycled due to contamination and multi-material composition

## Slide 5
Pre-filtering System (HCMR, Waste Et Water Sarl)
low-cost, automated and self-cleaning
lab-scale filtering system
Macro and micro-plastic litter
Photocatalytic Device (KTH Stockholm)
lab-scale photocatalytic device
Degrades micro-plastics in water under natural or artificial sunlight
Application after pre-filtering device
Technological solution for cleaning Micro Plastics

## Slide 6
CLAIM Micro plastic Observations: 17 profiles (BS)
Mesh size: 100/200/330μm at Gulf of Finland
150μm at Bornholm
Units: item per m3
Shape (fragment, fiber, pellet, foam, film)
Size (<1mm, 1mm,…,5mm, >5mm)
Polymer (PE, PP, EVA, PVA, Pest, PVC, EPDM,
PA, AC, PU, PMMA)
Measured concentration in the BS are rather low:
Order of magnitude 1 to 10 item/100m3
Roughly 10 times higher abundance in the Med Sea
CLAIM historical obs. data base: 59 profiles (BS)
Harmonization and Integration of observation data
Master thesis of Ella Jacobsen
CLAIM monitoring:
Number of Data Sets
12
15
5
6
10
7
Manta Net
Surface
CLAIM monitoring of Micro Plastics at Sea
150μm
100/200/330μm

## Slide 7
Med. Sea: Piraeus - Heraklion, Tunis-Marseilles, Tunis-Genoa
Baltic Sea: Tallinn – Helsinki
automated seawater sampling device and passive flow-through filtering system
passed a laboratory test on coastal waters, onboard tests on R/V vessel undergoing navigation.
Ferryboxes
CLAIM monitoring of Micro Plastics at Sea

## Slide 8
Mass distribution over size classes for different plastic types.
15% in size class 300μm (~measured at sea)
      85% in size class 42μm (average size, WWTP efluents)
      10319 t/y in size class 5μm (Tyre Wear, fraction that passes WWTP)
    The concentration of micro plastics in the river runoff is constant in time. The micro plastic load scales linearily with the river runoff.
River related inputs into the Baltic Sea
1000 t/y
BS estimates range from 887 t/y to 5453 t/y,
dependent on the WWTP cleaning factor

## Slide 9: Modelling micro plastic
Hydrodynamic: 7-8min for a 24h run with 320 cores.
With eulerian tracer routine: 11.5min on 540 cores
HBM: 3D baroclinic ocean and sea ice model + Eulerian tracer advection model
Eulerian passive tracer advection, now including the effect of sinking and raising.
Simple chl-a dependent biofouling model implemented.
First implementation of wave induced drift
900m
5km
1,8km
HBM setup: Combination of DMI operational storm surge set-up in the North Sea (boundary conditions) and extended high resolution Baltic Sea domain.
depth [m]
number of grid points
26 million grid points =17.9GB memory
100m 200m 300m 400m
64GB on each node available
122 layers

## Slide 10
Profile of zonal currents in the Gulf of Finland
Profile of meridional currents in the Gulf of Finland
Model
Model
ADCP
ADCP
Validation station 25o 1.5’E, 59o 43.3’N 25, near Tallin.
HBM model verification
Bias(u)
Bias(v)
RMSE(u)
RMSE(v)

## Slide 11: Vertical tracer dynamic, i.e. sinking or raising of micro plastics (no biofouling)
Stokes formula for sinking velocity
Tyre Wear is heavier than sea water
( and sinks down to the sea bed.
 | Tyre Wear | PCCP | Water
Density (ρ) [kg/m3] | 1250.0 | 965.0 | 1027.0
Radius (R) [10-6 m] | 5.0 | 3.0 | 
PCCP is lighter than sea water
( and raises due to his buoyancy to the sea surface.
ρ=density, R=radius, μ=dyn. visc.
Tyre Wear
PCCP

## Slide 12
Time series of Tyre Wear micro-plastic concentration in the Baltic Sea
Micro plastics are ….
easy to spread and nearly everywhere in the Baltic Sea after a few month.
Seasonal pattern are established; due to
      annual river runoff cycle
sinking/sedimentation in summer and enhanced mixing in winter
Tyre wear plastics is heavier than sea water and sinks to the bottom of the Baltic Sea.
PCCP micro plastics are lighter than sea water and are floating near the surface.
2 years run 2015,2016, initialised with zero concentrations
Tyre Wear micro plastics
Cosmetic Products (PCCP)

## Slide 13
Summer:
Tyre wear is heavier than sea water and sinks to the bottom of the ocean, where it forms layers of higher concentration in the Gothland deep and the southern Baltic Propper.
Sedimentation is implemented as a slow removal process
Winter:
Mixing and transport is further removing the tyre wear concentration near the sea bed.
Vertical dynamic of Tyre Wear
Surface Near the seabed
Summer
Winter
Contours mark areas with concentrations larger
thang/m3

## Slide 14
Micro plastic from cosmetic products (PCCP) are lighter than sea water and keep floating, until biofouling increases their density sufficiently enough.
The effect of biofouling has been studied using a simplified model for the biofilm growth.
A more comprehensive model for biofouling (Kooi et al 2017) model has been tested as a seperate model. It has not been implemented into HBM yet.
Vertical dynamics of PCCP
Surface Near the seabed
Summer
Autumn
Contours mark areas with concentrations larger
thang/m3

## Slide 15
with
Simplified biofilm growth model
Biofouling: Simplified model for biofilm growth
Saturated growth function for biofilm thickness
is advected as a “passive” tracer and is transported vertically by sinking/raising
The simplified model does not take into account:
 encounter and growth of algae in the sea water
 no seasonality, i.e. light, temperature dependency
 North Sea boundary input
Biofouling, a simplified approach

## Slide 16
after
1 month
after
6 month
Effects of Biofouling: (simplified model)
Enhanced effect of biofouling and sinking in the Southern Baltic Sea and the eastern Gulf of Finland; due to higher micro plastic concentrations.
Chl-a dependent growth fuction:
growth limiter of 1.1mg/m3 implemented, to include seasonality
develop chl-a dependent growth functions
Further development:
Implement a biofilm growth model (Kooi et al 2017), including
encounter of algae
light and temp. dependent growth functions
grazing and respiration.

## Slide 17
Motivation:
seasonally varying pattern of biofilm growth
improved vertical localization of biofilm growth in the euphotic zone
Implementation
chl-a concentration dependent growth limiter: 1,1 mg/m3
Considers only surface concentrations
Further upgrades, next steps:
chl-a dependent growth function
full 3d implementation
light attenuation dependent growth of biofilm
Biofouling, a first step towards a chl-a (algae) dependent growth function
Seasonal pattern of chl-a in 2015,
CMEMS reanalysis product

## Slide 18
Interesting for NOOS
source mapping methods and results
micro plastic monitoring technologies, ferry boxes, mantra net
Plastic pollution combatting technologies
Methods for harmonization and integration of diverse micro plastic observations into one data base.
Micro plastic modelling methods and results
Some open questions, currently unresolved processes
Open questions, unresolved processes
Sources: Seasonally varying micro plastic concentrations, retention in rivers
Resuspension/erosion of sediments and related micro plastic input near the sea bed (wave induced mixing)
Further developments
Biofouling model, including the occurrence of algae
Wave induced pollutant drift: 3D implementation, 2-way coupling

## Slide 19
THANK YOU
QUESTIONS?

## Slide 20
Wave induced drift of plastic pollutants.
WAM-HBM, 1-way coupled model: Waves have been implemented as a driving force to the surface ().
Wave induced
surface currents
Dec 2013
Wave induced
Concentration
changes
Dec 2013
Wave induced transport:
reduced conc. along the southern and eastern shores
enhanced release of micro plastics from the Odra delta
PCCP plastics,
3 month of simulation

## Slide 21
South North
West East
Entire Baltic Sea
Time series of Tyre Wear micro-plastic concentration in the Baltic Sea
0.31 mg/m2
0.076 mg/m2
0.16 mg/m2
0.034 mg/m2
0.094 mg/m2
0.383 mg/m2
0.31 mg/m2
0.1 mg/m2
0.206 mg/m2
0.13 mg/m2
0.277 mg/m2
2.72 mg/m2
Maximum surface concentrations (blue) for each domain are given in each figure.

## Slide 22
22
South North
West East
Entire Baltic Sea
Time series of PCCP micro-plastic concentration in the Baltic Sea

## Slide 23: River related inputs into the Baltic Sea, example PCCP
Figure above: Baltic Sea river run-off [m3/s] with color coded river input of tyre wear related micro plastics [g/s] of the 455 rivers considered in the model setup. The two rivers with the largest micro plastic contribution (red) are the Oder (1-th) and Vistula (2-nd).
Figure above: Tyre wear related micro plastic concentration [milli g/s] in the Baltic Sea.
Main assumption:
The concentration of micro plastics in the river runoff is constant in time.
Consequentially, the mass of micro plastic scales linearily with the river runoff.
River input values for tyre wear and pccp have been derived from the annual mean values in CLAIM D1.2

## Slide 24: Outlook(1): Parameterisation of Biofouling
Biofouling as a process to remove small plastic particles (PCCP) from the surface. (Kooi et al 2017)
The model consideres:
The encounter of algae along the way up and down the water column
The growth of algae (light dependent)
Gracing (mortality) of algae
Water temp. Dependent respiration
The concentration of algae has been calculated from Chl-A reanalysis concentrations. The conversion factor depends on water temperature and light intensity (PAR).
Number density (A) of algae per surface
Biofouling model at one location in Gothland deep: year 2015

## Slide 25: Biofouling effects on the vertical dynamic
Surface concentration of PCCP in the Baltic Sea (left) and concentration change due to biofouling: 1-th of May (middle) and 1-th of June (right). After 4 month of simulation bioactivity is starting to have an effect on the surface concentration values (middle). Over this time, the radius of plastic-algae particle has become sufficiently large, so that it is fastly removed from the surface.

## Slide 26
Shear Stress at
the sea bed
Fine Sediment
concentration in
the sea bed
SPM concentration
at the surface
Re-Suspension
Erosion
Sedimentation
Outlook(3): Resuspension and upwards mixing
Processes:
Sinking versus mixing
Advection
Sedimentation
Re-suspension
Erosion
Consumption
Bioturbation
3 SPM fractions:
wsink(f1)=0.0001 m/s
wsink(f2)=0.00002 m/s
wsink(f3)=0.001 m/s
SPM model