## Slide 1: Met Office activities in the NOOS region
Presentation to NOOS annual meeting; 3rd December 2021

## Slide 2: Operational Systems
3D baroclinic ocean models
  AMM15, 1.5km shelf enabled regional baroclinic FOAM-NEMO model for Northwest European Shelf; nested in regional open ocean model (FOAM-NEMO North Atlantic) and CMEMS Baltic model, forced by ECMWF and two-way coupled with WAVEWATCH III; 1x daily cycle generating 2 day analysis and 7 day forecast
  AMM7, 7km shelf enabled regional baroclinic FOAM-NEMO model for Northwest European Shelf; nested in regional open ocean model (FOAM-NEMO North Atlantic) and CMEMS Baltic model, forced by Global UM and one-way coupled with ERSEM to produce biogeochemical data; 1x daily cycle generating 2 day analysis and 6 day forecast
Surge and wave models
  NEMO-surge AMM7, 7km shelf enabled barotropic NEMO model; run in tide-only and tide+meteorology forced modes to enable estimation of meteorological effect on sea-surface height (surge residual), forcing from Global UM (deterministic) and MOGREPS-G (ensemble); 4x daily cycle generating up to 7 day forecast for 18 ensemble members (ensemble usually applied as lagged forecasts from consecutive cycles; 36 members)
  UK Waters WAVEWATCH III model on 3-1.5km SMC grid (AMM15 domain); nested in global WAVEWATCH III and forced by Global UM and AMM15 surface currents; 4x daily cycle generating 2.5 day forecast
  Global WAVEWATCH III model on 25-12-6-3km SMC grid (12-3 km cells in NOOS region); forced by Global UM; 4x daily updates generation 2.5-6 day forecast
  Atlantic WAVEWATCH III ensemble model on 25-12-6-3km SMC grid (12-3km cells in NOOS region); forced by MOGREPS-G; 4x daily cycle generating up to 7 day forecast for 18 ensemble members (ensemble usually applied as lagged forecasts from consecutive cycles; 36 members)
Re-analysis
  AMM7 NEMO-ERSEM ocean physics-biogeochemistry reanalysis from 1993-present, forced by ERA5
  AMM15 WAVEWATCH III model on 3-1.5km SMC grid, hindcast from 1980-present, forced by ERA5

## Slide 3: Recent updates to operational models
OS44 (live at 8th Dec 2020); PS45 (due live March 2022)
Wave and surge
  OS44 - Retirement of WWIII vn3.14 European 8km model; products replaced by 6km gridded data cut-out from 25-12-6-3km global model (similar 6km ensemble also available)
  PS45 - Update wave models to WWIII vn7.12 (ahead of public release)
  OS44 - Retired CS3X surge ensemble – probabilistic surge forecasts from NEMO-surge AMM7 configuration
  OS44 (summer 2021) – Update of surge bathymetry to use 2D varying bottom friction
  40-year ERA5 based surge hindcast generated
Bottom friction coefficients derived from Thetis model adjoint

## Slide 4: Recent updates to operational models
OS44 (live at 8th Dec 2020); PS45 (due live March 2022)
Shelf Seas
  OS44 – AMM15 uses two way coupled ocean-wave scheme (currents -> wave; ocean stress, Stokes, Hs -> ocean)
  OS44 – AMM7 biogeochemistry includes chlorophyll assimilation
  OS44 – AMM7 updated river inputs and SST bias correction
  PS45 – AMM15/AMM7 updated west/north boundary conditions to use CMEMS GLO-HR inputs (PSY4 introduces SSH change)
  PS45 – AMM15 uses hourly ECMWF forcing
  PS45 – Met Office NWP models will use forecast SSTs from AMM15 as surface temperature boundary condition
Improvement in Doodson filtered SSH residuals at Sheerness due to coupling
Chlorophyll improvement with DA

## Slide 5: Copernicus Marine Service – Northwest European Shelf MFC; updates in 2020-21
2020
  addition of total chlorophyll data assimilation at the forecast system;
  provision of wave hindcast (1980-2019);
  implementation of coupled ocean-wave forecasts, significantly improving the accuracy of the horizontal velocities fields;
  new physics and biogeochemical reanalysis time series (1993-2019) produced with an ocean-biogeochemistry coupled suiteand assimilation of Phytoplankton Functional Types (PFTs).;
  intercomparison of the NWS, IBI and Global reanalysis Multi Model Ensemble in the overlapping domain .
  new OMI for temperature and salinity anomalies, based on NWS reanalysis and study contribution to the Ocean State Report 4: “Using CMEMS satellite and model data to help assess eutrophication status in Northwest European Shelf Seas”
2021
  forecast products monitoring and inter-comparison with the BSH Multi-Model Ensemble (MME) forecast system.
  extensions (to mid 2021) of the physics-biogeochemistry reanalysis and wave hindcast
  OMI extension
  preparations for implementation of AMM7 and AMM15 configurations with Atlantic lateral boundaries from CMEMS GLO-HR

## Slide 6: Copernicus Marine Service – Northwest European Shelf MFC
Status of service bid for 2022
  Current consortium (Met Office, NOC, PML, BSH) provided a bid for continuation of service in Phase2 of Copernicus – start date 01 Jan 2022
  The process has been complicated by a delayed agreement of UK’s contribution to the space protocol
  At point of presenting outcome of bid review by MOi and EC procurement board pending
User statistics for NWS products in Copernicus Marine

## Slide 7: Planned developments
2022 will be a freeze year for operational model upgrades, due to Met Office transition to new supercomputer
Anticipated updates in 2023/24:
  Updated SLA assimilation on-shelf (2023)
  AMM15 to NEMOv4 and update Baltic boundary condition (2023)
  Copernicus Marine AMM15 ocean-wave forecasts extended to 10 days and 2x daily cycling (2023)
  AMM15 ocean-wave forecasts include wetting and drying scheme and Multi-Envelope Vertical Coordinates (2024)
  Improved wind pre-processing for wave refined (SMC) grids (2023)
  Assimilation of regular glider transect in central North Sea (2023)
  Updated BGC DA package (2023)

## Slide 8
New vertical coordinates for AMM15
  paper under review for fully assessed system in AMM7, now implementing and assessing in AMM15
Key Outcome of new vertical coordinates plus wetting and drying:
  Represent wetting and drying over beaches
  Removal of existing 10 metre min bathy limitation
  Reduced Horizontal Pressure Gradient errors
  Removal of sawtooth bathymetry at shelf break
  Improved model representation of stratification
Quasi-Vanishing terrain-following levels with .
Red indicates undesirable large slopes in the coordinates
Model bathymetry may present unrealistic saw-tooth patterns over the shelf and shelf-break
Multi Envelope s-coordinate system (Bruciaferri et al. 2018, 2020) with 2 envelopes:
Above 250 m: 25 s-levels with Siddorn & Furner 2012 stretching function following an envelope bathymetry with
Below 250 m: 26 s-levels following an envelope bathymetry

## Slide 9: Questions?